## Slide 1
Power And Data Movement GitHub: https://github.com/jasongraalum/CS533_Spring2018_Group2_Project
- Alex Kelly
-Ajinkya Shinde
-Jason Graalum
-Shikha Shah

## Slide 2
Goals:
Write benchmark codes that target specific configurations expected to be power efficient or power inefficient.
Conduct a study using the benchmarks to actually measure the power consumption.

## Slide 3
Hypothesis & Decision
Assumed that power consumption increases with the increase in data movement and makes code less efficient with degradation in performance.
Well, How to measure?

## Slide 4
Methodology
Three Cases
Baseline(red line)
  Load data into core and operate
L1 Cache Loads(orange line)
  On each operation, load data from L1 to core
LLC Cache Loads(green line)
  On each operation, load data from LLC to L1 to core

## Slide 5
Data Movement
Initialization
  For all cases, we need a consistent configuration cost
  Memory allocation and initialization
  Array size == 2X L1 Cache Size
Baseline
  Simple operation(addition) on value in core registers
L1 Cache
  Alternate between two L1 cache lines
LLC
  Load from a new cache line on each access
  Twice as many cache lines in the array as in L1
  Guarantees that every load causes a L1 cache miss

## Slide 6
Experimental Setup
Used bash script to run multiple cases
Took photo of power meter in between each run
Found good use for Algorithms Textbook

## Slide 7
Power per L1 Cache Load
Chart: 
| 800 | 1600 | 3200 | 6400
out_case1 - Sum of Power_per_L1Load | 2.6106e-10 | 2.3912e-10 | 2.3033e-10 | 2.1862e-10
out_case2 - Sum of Power_per_L1Load | 4.394e-10 | 3.8802e-10 | 3.4773e-10 | 3.4935e-10
out_case3 - Sum of Power_per_L1Load | 4.042e-10 | 4.1509e-10 | 4.0426e-10 | 4.1887e-10
out_case1 - Sum of L1-dcache-loads | 22983350584 | 92004863113 | 369031464738 | 1472852489603
out_case2 - Sum of L1-dcache-loads | 29585881773 | 118551079469 | 474508425268 | 1894928860721
out_case3 - Sum of L1-dcache-loads | 49480759723 | 197547152231 | 791571422569 | 3163291942885

## Slide 8
Power per LLC Cache Load
Chart: 
| 800 | 1600 | 3200 | 6400
out_case1 - Sum of Power_per_LLCLoad | 9.7153e-07 | 1.757e-06 | 1.161e-06 | 2.1023e-06
out_case2 - Sum of Power_per_LLCLoad | 1.5428e-06 | 1.8875e-06 | 1.6753e-06 | 2.1506e-06
out_case3 - Sum of Power_per_LLCLoad | 1.1695e-06 | 1.8117e-06 | 1.3902e-06 | 1.8776e-06
out_case1 - Sum of LLC-loads | 6175824 | 12521227 | 73215294 | 153169022
out_case2 - Sum of LLC-loads | 8426342 | 24370674 | 98490098 | 307816670
out_case3 - Sum of LLC-loads | 17100654 | 45261611 | 230187184 | 705672882

## Slide 9
Real-World(ish) Data-Flow Cases:
What kind of data-intensive applications are common in the wild?
  Databases
  Analytics / Machine Learning
  Network traffic
How do different data-flow patterns in these cases affect power/performance?
How can we test something like this?

## Slide 10
Big Data: Map, Filter, Reduce
Simple high-level algorithms for dealing with massive data asynchronously
One of the most popular cases of functional programming used in practice
Google and Amazon like these a lot
Used everywhere all the time

## Slide 11
NLP: Markov-chain N-Gram
Very simple but powerful probabilistic natural language model
Build a probability model of all possible next words given a sequence of N words
Underpins a lot of machine translation, text synthesis, and sentiment analysis
Lots of data to crunch: Needs huge corpuses to be even remotely useful

## Slide 12
Markov Ouroboros: “Realistic” test
Process a big corpus of data (Tweets)
Filter and Map to generate n-grams, then stack them with a reduce step
Build a simplistic markov-chain bigram model with all the data
Sample new text from the model and feed it right back through the first step

## Slide 13
Markov Ouroboros: Why?
Moves a whole bunch of data around
Different kinds of data processing
  Aggregation
  Filtering
  Comparisons
Highly entropic data, so likely to cause cause cache misses

## Slide 14
Markov Ouroboros: Cases
Baseline: Do it on one core
  How much power does just spinning up the python runtime take?
Parallel: Split the data, put it on 4 cores
  With full processor utilization, how much more power do we use?
Cascading: Move the data between cores
  Does moving the data around increase power consumption?

## Slide 15
Markov Ouroboros: Details
Does the size/amount of data matter?
  Cache vs Memory
What about complexity?
  Will the power usage go down if the models regulaize the data?
Controlling for the disk read
What kind of processing do you cascade?
  Different steps?
  “Juggling” data?

## Slide 16
Markov Ouroboros: “Results”
Working test case, but...
Power monitor stopped working
Only subjective results
Spoilers: Different processes are a hard test case to get right
But working test code which we will make available if anyone’s curious

## Slide 17
Results
Add Graphs

## Slide 18
Conclusion
Explain Result

## Slide 19
References

## Slide 20
Back up slides

## Slide 21
Raspberry Pi 3
Why did we use a Raspberry Pi 3?
  Ease of use
    Easy Access
    Easy Configuration
  Power measurement through USB power supply
Was it a good decision?
Notes: <number>