## Slide 1: Power And Data Movement GitHub: https://github.com/jasongraalum/CS533_Spring2018_Group2_Project
- Alex Kelly
-Ajinkya Shinde
-Jason Graalum
-Shikha Shah

## Slide 2: Goals:
Write benchmark codes that target specific configurations expected to be power efficient or power inefficient.
Conduct a study using the benchmarks to actually measure the power consumption.

## Slide 3: Hypothesis & Decision
Assumed that power consumption increases with the increase in data movement and makes code less efficient with degradation in performance.
Well, How to measure?

## Slide 4: Methodology
Three Cases
Baseline(red line)
  Load data into core and operate
L1 Cache Loads(orange line)
  On each operation, load data from L1 to core
LLC Cache Loads(green line)
  On each operation, load data from LLC to L1 to core

## Slide 5: Data Movement
Initialization
  For all cases, we need a consistent configuration cost
  Memory allocation and initialization
  Array size == 2X L1 Cache Size
Baseline
  Simple operation(addition) on value in core registers
L1 Cache
  Alternate between two L1 cache lines
LLC
  Load from a new cache line on each access
  Twice as many cache lines in the array as in L1
  Guarantees that every load causes a L1 cache miss

## Slide 6: Experimental Setup
Used bash script to run multiple cases
Took photo of power meter in between each run
Found good use for Algorithms Textbook

## Slide 8: Map / Reduce & Markov Model (Application – Core to Core Data Movement)
Baseline
Split Data
Core to Core
Notes: Why was it chosen , what motivated us to do that
Process of testing :
a. Baseline
i. Move all data into L1 cache and LCC from main memory
ii. Data set should be large enough that multiple cache misses will occur
iii. Execute 4 operations on all the data on a single core.
iiii. Store data in main memory from single core L1
b. Split Data
i. Move ¼ of the data from main memory into L1 cache of each core
ii. Execute 4 operations on all the data in each core
1. Large data – multiple fills of L1 cache
iii. Store data in main memory from each core L1 cache
c. Core to Core
i. Move ¼ of the data into each L1 cache of each core
ii. Execute 1 operation in each core
iii. Store data back in main memory
iv. Shift data to each core and repeat for each of the 3 remaining operations

## Slide 9: Results
Add Graphs

## Slide 10: Conclusion
Explain Result

## Slide 11: References

## Slide 12: Back up slides

## Slide 13: Raspberry Pi 3
Why did we use a Raspberry Pi 3?
  Ease of use
    Easy Access
    Easy Configuration
  Power measurement through USB power supply
Was it a good decision?